## Slide 1
ESCALATE TRAINING PROGRAM · SUMMER 2026
BGP Control Plane Measurement
Week 2: from the global routing table to who owns and who reaches the Internet’s address space.
PLENARY
Tue Jun 23 · 12:00 PT
INSTRUCTOR
kc claffy
SENIOR MENTORS
Ricky Mok · Bradley Huffaker · Rocky Chang
PROGRAM CONTACT
Alex Ma
Supported by the NSF ESCALATE project · OAC-2519416
Notes: Infrastructure-hour lab background for the nids-bgp-control-plane assignment. Three tasks: origin AS / address attribution, customer-cone reach, and ranking joined to organizations.

## Slide 2
THE ARC
Ten building blocks — you are here
WEEK 2 · BUILDING BLOCK 2 / 10
1
Internet structure & ASNs
2
BGP at scale
3
Registries: WHOIS / IRR / RPKI
4
Traceroute, ITDK
5
DNS
6
Geolocation
7
Network telescope
8
Data fusion (IYP)
9
Degradation forensics
10
SDSC hackathon
Weeks 1–8 build one block at a time; weeks 9–10 integrate them into a full forensic pipeline.
ESCALATE Training Program · Summer 2026
Notes: This lab is Block 2, BGP at scale. Task 2 (customer cones) borrows from Block 4 — flagged on the cone slide as a forward-pointer; the full relationships/cones treatment lands in Block 4.

## Slide 3
LAST WEEK · RECAP
From topology to address space
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Block 1 mapped Internet structure — ASes, ASNs, and how they interconnect.
You worked the topology view: who connects to whom.
We deferred the next question: who owns and who reaches the address space.
THIS WEEK BUILDS ON IT
We read the global routing table to attribute every prefix to an origin AS — then to the cone that reaches it.
Notes: Orient, don't re-teach: this bridges Block 1's topology view into Block 2's address-space view.

## Slide 4
PART ONE
01
From RIB to origin AS
Reading the global routing table to attribute address space.
Notes: Part one: origin-AS attribution and address counting (Task 1).

## Slide 5
TASK 1 · FRAMING
BGP as a system, not just a protocol
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
BGP is a protocol for inter-domain routing — we analyze it as a system of global reachability.
Measurement: how do we see the global routing state at one moment?
RIB (Routing Information Base): a collector’s snapshot of every route it has received.
who talks to whom
who owns & reaches what
this module shifts the question
Notes: BGP basics are INTERMEDIATE for this cohort (median 3) — brief grounding, then move to address space. Emphasize the topology→address-space shift.

## Slide 6
WHAT YOU’LL WORK WITH
Datasets & tools for this lab
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
RouteViews / MRT
Global routing tables archived by Univ. of Oregon collectors, as MRT (Multi-Threaded Routing Toolkit) binary records.
COLLECTOR · RIB
route-views3 · 2026.05
bgpkit
Decodes MRT so you iterate over routing records as Python objects.
TOOL
pybgpkit_parser
CAIDA customer cones (PPDC)
Per-AS customer-cone membership, derived from provider→customer links.
FILE
20260501.ppdc-ases.txt.bz2
AS2Org
Maps ASNs to real-world organizations and country.
STORED AS
as2org.jsonl
ESCALATE Training Program · Summer 2026
Notes: Names + identifiers in Roboto Mono. RouteViews/MRT confirmed snapshot route-views3 / 2026.03. IODA is an optional cross-check, not used here.

## Slide 7
TASK 1 · THE DATA
Anatomy of a RIB entry
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Each MRT record is one prefix announcement seen from one vantage point (peer):
Field | Example | Meaning
collector | route-views3 | which collector
peer_asn / peer_ip | 10 / 12.3.2.1 | the vantage point
as_path | 10 724 8234 | ASNs the route traversed
origin_asns | 8234 | last ASN — the originator
prefix | 192.0.2.0/24 | the announced CIDR block
The origin AS — the last ASN — is what we attribute address space to.
Notes: origin_asns is a set in bgpkit — usually one ASN, sometimes several. Several = MOAS (next).

## Slide 8
TASK 1 · ATTRIBUTION
The AS path: origin and MOAS
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Take the last ASN in the path — the origin AS, via elem.origin_asns.
Attribution: each prefix is credited to its origin AS — this drives the Task 1 counts.
MOAS: the same prefix shows different origins across the table.
# as_path: 10 724 8234 -> origin = last hop
for elem in bgpkit.Parser(url=url):
prefix_origins[elem.prefix] \
.update(elem.origin_asns)
Notes: Task 1 needs only the origin (last hop). The full path's link structure is what CAIDA uses upstream to build the cone file loaded in Task 2 — not reconstructed in this notebook.

## Slide 9
TASK 1 · MOAS
The Multi-Origin AS puzzle
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
A MOAS prefix is announced from more than one AS at once.
Benign: multi-homing, traffic engineering, mergers / acquisitions.
Security risk: can signal a BGP hijack — an unauthorized AS announcing someone else’s space.
Task rule: exclude MOAS from per-AS counting (can’t attribute cleanly). Ballpark < 1%.
if len(origins) > 1:
moas_count += 1
else:
asn = next(iter(origins))
Notes: Q2 asks for the MOAS percentage — real value ≈ 0.4%. If a student reports 10%+, the MOAS test is wrong (e.g. counting peers, not origins).

## Slide 10
TASK 1 · ADDRESS MATH
Prefixes vs. address space
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Counting prefixes is coarse — prefix size varies exponentially.
/8 → 16,777,216 addresses /16 → 65,536 /24 → 256
A few coarse blocks can dwarf thousands of /24s — we need an address count.
/8 block
/16
/24
addresses = 2 for a /n prefix
(32−n)
Notes: Plants the seed for Q3 (divergence). CIDR math is INTERMEDIATE; keep it brief.

## Slide 11
METHODOLOGY
Counting addresses: longest-prefix match
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Prefixes nest. Credit each address to the most-specific prefix covering it: take a prefix’s size and subtract the sizes of its direct children only.
THE HARDEST CORRECTNESS POINT
Direct children only. If A⊃B⊃C, A subtracts B (which already contains C); B subtracts C. Subtracting C from A too undercounts A.
Load
ipv4_single_origin
↓
Insert into trie
pytricia.PyTricia(32)
↓
Subtract direct kids
pyt.parent(child)==prefix
↓
Per-AS total
counts[asn]
Notes: Hardest correctness point in the lab. Walk the 3-level case slowly (also in the appendix).

## Slide 12
TASK 1 · IMPLEMENTATION
Longest-prefix match with PyTricia
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
pyt = pytricia.PyTricia(32)
for prefix, asn in ipv4_single_origin:
pyt[prefix] = asn
for prefix, asn, plen in parsed:
total = 1 << (32 - plen)
overlap = 0
for child in pyt.children(prefix):
if child == prefix: continue # children() includes self
if pyt.parent(child) == prefix: # DIRECT children only
overlap += 1 << (32 - int(child.split('/')[1]))
counts[asn] += total - overlap
Scale check: total attributed IPv4 ≈ 3.1 billion across ≈ 77,600 origin ASes (not ≈ 4.3B — that means double-counting).
Notes: Two gotchas: children() includes the prefix itself; filter to direct children. Off-by-billions means nested space double-counted.

## Slide 13
TASK 1 · READING SHAPES
Reading a CCDF
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
A CCDF plots, for each value x, the number of ASes with ≥ x.
Log–log axes — counts span 8+ orders of magnitude.
Steep left + long tail = a few heavy hitters dominate;
a near-straight line ≈ power law.
Notes: Each point means “this many ASes have at least x.” Stress at least. CCDF is lab-specific — teach it here.

## Slide 14
TASK 1 · OUTPUT
Origin metrics, and Q1 / Q3
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Metric | min | max | mean | median
Origin prefix count | 1 | ~14.4k | ~14 | 2
Origin address count | 8 | ~223M | — | —
Q1 — shape: heavy-tailed; most ASes tiny (median 2), a few enormous (mean 14, dragged by the tail).
Q3 — divergence: the curves separate because prefix size varies hugely — the top-prefix AS is not the top-address AS.
Notes: Mean 14 vs median 2 is the Q1 headline. Calibration figures real but rounded; exact answers withheld.

## Slide 15
PART TWO
02
Customer cones & reach
From what an AS announces to what its cone can reach.
Notes: Part two: customer cones (Task 2).

## Slide 16
TASK 2 · CONES
The customer cone
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Customer cone = the root AS plus every AS reachable via provider→customer links.
Measures transit influence — not just what an AS announces itself.
Input: CAIDA PPDC file 20260501.ppdc-ases.txt.bz2, loaded as a black box.
You use the precomputed cone file here; how relationships & cones are inferred is Block 4.
This graph shows the respective cone sizes for each AS
Notes: Root is in its own cone → a stub's cone is just itself → cone == origin for stubs. Anchors Q5.

## Slide 17
TASK 2 · TWO COUNTS
Owns vs. reaches
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Task 1 — origin
what an AS owns
Question: who owns the space?
Nested more-specifics: subtracted (LPM)
Method: PyTricia children-subtraction
Task 2 — cone
what an AS reaches
Question: what does the cone reach?
Nested more-specifics: NOT subtracted
Method: sorted-interval sweep
Notes: The dual-method distinction is the biggest correctness gap. Owns (subtract) vs reaches (don't subtract).

## Slide 18
TASK 2 · COUNTING
Counting the cone: prefix sum + address sweep
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Cone prefix count — sum members’ prefix counts
cone_prefix_count[root] = sum(
asn_prefix_count.get(m, 0)
for m in members)
Cone address count — merge nets into runs
nets = sorted(member_nets, key=...)
total, covered_end = 0, -1
for net in nets:
start = int(net.network_address)
if start > covered_end:
total += net.num_addresses
covered_end = start + \
net.num_addresses - 1
Within a cone we ask “is this reachable through me?” — so we do not subtract more-specifics. The deliberate opposite of Task 1.
Notes: Address sweep merges sorted intervals; no more-specific subtraction.

## Slide 19
TASK 2 · OUTPUT
Cone metrics, and Q4 / Q5
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Metric | min | max | mean | median
Cone prefix count | 1 | ~893k | ~203 | 3
Cone address count | 8 | ~2.35B | — | ~1k
Q4 — shape: even more heavy-tailed (median cone 3; the top cone reaches hundreds of thousands).
Q5 — why cone ≥ origin: the cone is a superset of the AS itself (equal only for stubs). Providers reach customer prefixes they don’t originate — so cone count dwarfs origin count.
Notes: Q5 hinges on superset → cone ≥ origin, equal only for stubs. Largest origin ≈14.4k vs largest cone ≈882k.

## Slide 20
PART THREE
03
From numbers to organizations
Who are the leaders — and why they rank where they do.
Notes: Part three: ranking and AS2Org (Task 3).

## Slide 21
TASK 3 · ORGS
Map ASNs to organizations (AS2Org)
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Join the numeric leaders back to real-world orgs using CAIDA as2org.jsonl (orgName, country, members).
One organization can hold many ASNs — clustered from registry records.
Kind | Example | Ranks high via
Transit backbone | Lumen / L3 | huge cone
Cloud / content | Amazon | own prefixes / addresses
Legacy holder | US DoD | coarse address blocks
Notes: Leader TYPES, not the answer key. Real ranked table and counts are [student computes].

## Slide 22
TASK 3 · RANKING
The rank-vector sort
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
1.
Rank each metric independently (rank 1 = highest).
2.
Union the top-3 ASNs across the four rank dicts.
3.
Sort rows by each ASN’s sorted vector of ranks — best first.
def ranked(d):
return {asn: r for r, (asn, _) in
enumerate(sorted(d.items(),
key=lambda x: x[1],
reverse=True), start=1)}
[1,1,3,4] beats [1,2,2,3] beats [2,2,3,9999] — compare best rank, then next. Being #1 in two metrics beats #1 in one.
Notes: The rank-vector sort is what trips students up. #1 in two metrics outranks #1 in one.

## Slide 23
TASK 3 · OUTPUT
Q6: one sentence per top-4 organizations of eac type
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Transit backbone — ranks via cone (prefixes + addresses), needn’t own much itself.
Cloud / content — ranks via own address count (large hosting allocations).
Legacy holder — ranks via address count from historic coarse blocks, modest cone.
The exact four orgs and counts are [student computes] — name the mechanism, not just the org.
Notes: A good Q6 names the mechanism (transit vs ownership vs legacy), not just the org name.

## Slide 24
BEFORE YOU RUN IT
Common pitfalls
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Don’t double-count nested space — total ≈ 3.1B, not ≈ 4.3B.
Task 2 sweep does NOT subtract more-specifics — the opposite of Task 1.
Use .update(origin_asns) not .add(); exclude MOAS; CCDF y = ASes with ≥ x (log–log).
Ranking unions top-3 across metrics, sorted by the rank vector.
Notes: Run this before students leave for JupyterHub. Orange marks the two costliest correctness traps.

## Slide 25
ASSIGNMENT 2 · DUE BEGINNING OF WEEK 3
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
nids-bgp-control-plane
Attribute address space from the global routing table, measure cone reach, and rank the leaders — the BGP section of your module.
Task 1 — origin map, MOAS %, LPM address counts, origin CCDF (Q1–Q3)
Task 2 — customer-cone prefix & address counts (Q4–Q5)
Task 3 — top-3-in-any-metric table joined to AS2Org (Q6)
Finish all notebook tasks and questions
MODULE MILESTONE
Becomes the BGP / control-plane section of your own training module.
REPOSITORY
github.com/CAIDA/ nids-bgp-control-plane
ESCALATE Training Program · Summer 2026
Notes: Assignment structure identical every week. Slug + repo in Roboto Mono. Authoritative grading lives in the Claude Code workflow, not here.

## Slide 26
BEFORE NEXT WEEK
This week, in five steps
WEEK 2 · BUILDING BLOCK 2 / 10
ESCALATE Training Program · Summer 2026
Open the notebook on NRP JupyterHub (jupyterhub-west.nrp-nautilus.io).
Work Tasks 1–3; replace each # YOUR CODE HERE.
Finish the assignment by the beginning of Week 3.
Attend the plenary — or catch up; materials are posted.
Use the hands-on hour and mentors for infrastructure help.
OPTIONAL BACKGROUND
RouteViews & MRT background; CAIDA AS Rank notes on customer cones — context, returns in Block 4.
Questions · Mattermost (fastest)
training-program-info@caida.org
ESCALATE Training Program · Summer 2026
Notes: Predictable close. Confirm NRP access before the session, not during. Questions line kept identical.

## Slide 27
APPENDIX · FOR SELF-STUDY
A
Supporting detail, not covered live
A few slides so the deck stands on its own.
Notes: Everything after this is self-study.

## Slide 28
APPENDIX · ADDRESS COUNTING
Longest-prefix match, three levels deep
ESCALATE Training Program · Summer 2026
Prefixes nest arbitrarily deep. Each address must be credited once, to the most-specific prefix that covers it, so a provider’s block is not counted on top of the customer more-specifics inside it.
Subtract direct children only. With A ⊃ B ⊃ C: A subtracts B (B already contains C), and B separately subtracts C. If A also subtracted C, A would be undercounted — C would be removed twice.
A = 10.0.0.0/8 (16,777,216)
B = 10.1.0.0/16 (65,536, in A)
A = 16,777,216 - 65,536 = 16,711,680
B = 65,536
/8 = A
/16 = B
/24 = C
ESCALATE Training Program · Summer 2026
Notes: Self-study detail for the LPM rule; denser text is fine here.

## Slide 29
APPENDIX · GLOSSARY
Advanced terms and acronyms
ESCALATE Training Program · Summer 2026
Program-, platform-, and research-specific terms used in this deck. (General terms like IPv4, BGP, AS, CIDR omitted.)
AS2Org
CAIDA dataset mapping ASNs to organizations (orgName, country, members).
bgpkit
Toolkit that parses MRT routing dumps into Python objects.
CCDF
Complementary CDF: for each x, the count of items with value ≥ x.
customer cone
Root AS plus all ASes reachable via provider→customer links.
LPM
Longest-prefix match: credit an address to its most-specific covering prefix.
MOAS
Multi-Origin AS: one prefix announced by more than one origin AS.
MRT
Multi-Threaded Routing Toolkit — binary format for archived routing tables.
origin AS
The last ASN in a BGP path — who announced the prefix.
OSDF
Open Science Data Federation — staging path used to fetch the RIB.
PPDC
Per-AS customer-cone membership file (provider→customer derived).
RIB
Routing Information Base — a collector’s snapshot of received routes.
RouteViews
Univ. of Oregon project archiving BGP tables from many collectors.
ESCALATE Training Program · Summer 2026
Notes: Advanced terms only; alphabetized; two-column reflow.